Florida Cluster

Part I - IP Addressing Scheme – 9 LANs, 10 WANs

Miami - 500 customers		Orlando/Disney - 900 customers	St. Petersburg - 33 customers

Naples - 100 customers		Daytona Beach - 47 customers	Gainesville - 12 customers

Tallahassee - 18 customers		Pensicola - 5 customers		Jacksonville - 230 customers

| Subnet Size | Network Address | First Usable | Last Usable | Broadcast | Subnet Mask |
| --- | --- | --- | --- | --- | --- |
|  | 190.X.144.0 |  |  |  |  |
| WAN 10 | 190.X.152.92 |  |  |  |  |

Part II.  Configuration Details

- IP Addressing Rules

  - The Router’s FastEthernet interface gets the first usable.

  - PCs get the LAST usable IP address of each LAN.

  - Disney server gets the last usable IP from the Orlando LAN.

  - DNS should be set to 8.8.8.8 for all devices.

  - Use the Note tool to label all WAN links (WAN1 to WAN10) in your topology.

- Router Configuration should include the following:

  - Hostname

  - Passwords:  enable secret (class), line console 0(cisco)

  - Telnet – Line vty 0 4 (cisco)

  - Save the configuration

  - Serial interfaces can be configured with clock rate of 4 Mbps.

- Routing Protocol

  - RIP version 2

  - Default Route should be built and propagated from Tallahassee towards Atlanta.

- Disney Server

  - Email Service

    - domain will be disney.com

    - The following accounts should be created with a password of 12345

      - mickey@disney.com

      - minnie@disney.com

      - walt@disney.com

      - goofy@disney.com

  - HTTP (Web Server) Service

    - Edit index.html to specify Disney.com

    - Add hyperlinks to other web servers

      - us.gov

      - nyse.com

      - palin.com

      - google.com

Testing – Within Florida

- All Florida devices should be able to PING one another

- Each router should have routes to all LANs and WANs, as well as 0.0.0.0 (default route)

- Disney website should be visible if IP address is used, but not domain name.

- HTTP using domain name and Email will not work until DNS in California is configured, as well as the backbone of the topology.