Hawaii Cluster – IP Scheme and Instructions

103.X.64.0 /19

Part I - IP Addressing Scheme (California) – 6 LANs, 5 WAN links

East Hawaii – 1500 hosts			West Hawaii – 1200 hosts		Oahu – 300 hosts

Maui – 450 hosts				Kauai – 200 hosts			Molokai – 105 hosts

| Subnet Name/Size | Network Address | Subnet Mask |
| --- | --- | --- |
|  | X.208.0.0 |  |

Part II.  Configuration Details

- IP Addressing Rules

  - The Router’s FastEthernet interface gets the first usable.

  - PCs on each LAN get 2nd, 3rd and 4th usable.

  - Switches get last usable IP address from each LAN.

  - Use the Note tool to label all WAN links (WAN1 to WAN5) in your topology.

- Router Configuration should include the following:

  - Hostname

  - Save the configuration

  - Make sure you set up:

    - Enable secret, Line console 0 (cisco), line vty (cisco)

  - Serial interfaces can be configured with clock rate matching that shown within the topology.

  - Be sure to all set your Bandwidth statements on all serial interfaces so EIGRP will properly calculate the correct cost to get to different parts of the topology.

- Routing Protocol

  - RIP (v2)

  - Set up RIP v2.  You should only need 1 network statement on each router.  Easy.

  - Hawaii is the border router and should create a default route (towards Phoenix).

  - Hawaii should use RIP to distribute the default route via Default-Information Originate

- Hawaii.com Web Server

  - Edit index.html as before

  - Add hyperlinks to the other web sites.  (a href)

  - Add DNS entry on google DNS server and Alaska DNS server for Hawaii.com

  - Add hyperlinks to for all websites on other web servers, 1 per line

- Access-Control Lists - You will create seven ACLs.  The details for each is:

| ACL# | Purpose |
| --- | --- |
| 22 | Block the Daytona beach LAN from reaching the Molokai LAN. Daytona should not be blocked from reaching any other LANs in Hawaii with this ACL. |
| 55 | Block New York Cluster and Michigan Cluster from reaching the WestHawaii LAN. This ACL should not block those clusters from reaching the EastHawaii LAN, nor should it block any other cluster from reaching the WestHawaii LAN. This ACL will block all kinds of traffic – (Pings, web, telnet, etc…) |
| 105 | O2 and K3 should be able to PING palin.com, but can't bring up the palin.com web page (port 80). All other hosts on the Oahu and Kauai LANs should be able to do both. This should be accomplished with a single ACL on a single router. (Placement is the key) |
| 134 | K2 and K3 should be able to PING Mo2 and Mo3, but not Mo1. Mo2 and Mo3 should be able to ping K2 and K3, but not K1. K1 and Mo1 should be able to PING one another. Don't block anything else, but what is specified above. |
| 156 | The Maui router should block any telnet session (port 23) that originates from outside Hawaii. Any telnet connection from inside Hawaii should be successful. |
| 180 | The EastHawaii LAN should only be able to be PINGed by devices that have .254 or .253 in the last octet of their IP address. (mostly server and switches) |
| 195 | The Molokai LAN should be able to send email, but not receive them, to anywhere in the US. No LAN in Hawaii should be able to FTP anywhere, except for Kauai. |

- Backbone - Add Hawaii cluster IP to the backbone routers.  (103.X.64.0 /19)

- Fresno – Add a static route to Hawaii out S0/2/0 (toward Phoenix)