Networking 1A – Basic Switch VLAN Commands

Assigning an IP Address to a Switch

IP addresses are assigned to a VLAN on a switch, usually the default VLAN (VLAN 1)

INTERFACE VLAN1

IP ADDRESS <IP Address> <subnet mask>

NO SHUTDOWN

Setting a Default Gateway on a Switch

IP DEFAULT-GATEWAY <IP Address of Router>

*You do NOT add a subnet mask to this command.

Creating a VLAN on a Switch

VLAN DATABASE

VLAN <VLAN #> NAME <VLAN name>		EX:  VLAN 10 NAME MARKETING

*This is done starting from privileged mode 			Switch#

You can remove a VLAN from the database with NO VLAN <VLAN #>, while modifying the database.

Assigning a Switchport to a Specific VLAN (Access Port)

This involves pointing the interface, setting it as an access port, then connecting it to a specific VLAN

INT F0/1

SWITCHPORT MODE ACCESS

SWITCHPORT ACCESS VLAN <VLAN #>		EX:  SWITCHPORT ACCESS VLAN 10

*Make sure that you have created the VLAN in the database before you try to connect a port to it.

Assigning a Switchport to All VLANs (Trunk Port)

A trunk port allows communication from ALL VLANs.  It is set up between switches and between switches and the router.

INT F0/8

SWITCHPORT MODE TRUNK