New York Cluster - IP Addressing Scheme – X+10.36.0.0 /14

Part I - IP Addressing Scheme – 10 LANs, 8 WANs

Albany - 3000 				NYC Lan # 1 - 18,000 		NYC Lan # 2 - 30,000

NYC Lan # 3 - 10,000 			Syracuse - 1000 			Watertown - 77

Massena - 300 				Buffalo - 1300 			Rochester - 880

Ithaca - 42

| Subnet Size/Name | Network Address | First Usable | Subnet Mask |
| --- | --- | --- | --- |
|  | X+10.36.0.0 |  |  |

Part II.  Configuration Details

- IP Addressing Rules

  - The Router’s FastEthernet interface gets the first usable.

  - PCs get the second usable IP address of each LAN.

  - nyse.com server gets the last usable IP from the NYC LAN# 3.

  - DNS should be set to 8.8.8.8 for all devices.

  - Use the Note tool to label all WAN links (WAN1 to WAN10) in your topology.

- Router Configuration should include the following:

  - Hostname

  - Serial interfaces can be configured with clock rate of 4 Mbps.

- Routing Protocol

  - Static Routing Only

    - Every router needs a default route, pointing toward Ithaca (and Ithaca to Cleveland)

    - Stub networks (Buffalo and NYC) only need the above default route.

    - Non-stub routers will need static routes to the other LANs within the New York Cluster

    - You may be able to minimize the number of static routes you build on these routers by utilizing the default route, when appropriate.

- NYSE.COM Server

  - Email Service

    - domain will be nyse.com

    - The following accounts should be created with a password of 12345

      - admin@nyse.com

      - donald@nyse.com

      - wolf@nyse.com

  - HTTP (Web Server) Service

    - Edit index.html to specify nyse.com

    - Add hyperlinks to other web servers

      - us.gov

      - disney.com

      - palin.com

      - google.com

  - FTP Service

    - Set up FTP service on nyse.com server

    - Create the following accounts with full privileges and password of 12345

      - admin, wolf

    - Create the following account with only read and list privileges

      - donald

    - There is a file on NYC-LAN#3 called secrets.txt that should

Testing – Within New York

- All New York devices should be able to PING one another.

- FTP should work if the nyse.com server IP address is used, but not the domain name.

- nyse.com website should be visitable if IP address is used, but not domain name.

- HTTP and FTP using domain name and Email will not work until DNS in California is configured, as well as the backbone of the topology.14