The OSI Model

Layer 1 – Physical Layer

- Media – The cabling used on a computer network.

  - Unshielded Twisted Pair (UTP)

    - 8 colored wires inside a plastic sheath

    - Three cable types

      - Straight Through Cable

        - Connects PCs to switches

        - Connects switches to routers

      - Crossover Cable

        - Connects pc to pc

        - Connects switch to switch

        - Connects PC to router

      - Rollover

        - Connects PC to router for configuration purposes

  - Coaxial

    - Solid copper core

    - Two types

      - Thicknet – 10Base5

      - Thinnet – 10Base2

    - Half Duplex – Data can only be sent in one direction at a time

  - Fiber Optic

    - Sends a light signal instead of electrical

    - Immune to EMI (Electromagnetic Interference)

    - Can travel extremely long distances without weakening

    - Bandwidth capacity is limitless

    - Typically used for network backbones

- Signaling on the Media

  - Binary

    - Copper Media (coaxial and UTP)

      - 1 – 5 volt pulse

      - 0 – Low level or 0 volt pulse

    - Fiber Optic

      - 1 – High intensity light pulse

      - 0 – Low level or absent light pulse

- PDU – Bit (what we call the data at the physical layer)

Layer 2 – Data Link Layer

- LAN (Local Area Networks) are defined here.

  - Types of LANs

    - Ethernet

      - Most Common

      - Different speeds have different names

        - Ethernet – 10 Mbps (10,000,000 bits per second)

        - FastEthernet – 100 Mbps

        - Gigabit Ethernet – 1 Gbps (1 billion bps)

      - Ethernet Standards

        - 10Base2 – 10 Mbps, Thin coaxial,  “Thinnet”

        - 10Base5 – 10 Mbps, Thick Coaxial, “Thicknet”

        - 10BaseT – 10 Mbps, UTP

        - 100BaseT – 100 Mbps – UTP

        - 1000BaseT – 1 Gbps – UTP

        - 1000 Base LX, 1000BaseSX – 1 Gbps, Fiber Optic

      - CSMA/CD – Carrier Sense Multiple Access/ with Collision Detection

        - When a network wants to transmit, it first “listens” to the media.

          - If no signal is present, the device transmits

          - If a signal is present, the devices waits.

        - When two machines transmit at the same time, a collision occurs.

        - When a collision occurs the following happens:

          - The PC nearest the collision will sense it.  (10 volts)

          - The PC issues a jam signal telling all PCs to stop transmitting.

          - All PCs then run a backoff algorithm, which means:

            - Each PC waits a random amount of time

            - Random time staggers the devices

          - After the backoff algorithm, normal activity resumes

    - Token Ring

      - Ring Topology

      - An electronic token circles the network.

      - Only the PC with the token can transmit.

      - No possibility of collisions.

      - Downside is that you must wait for the token to transmit.

      - Not efficient on larger networks.

    - FDDI – Fiber Distributed Data Interface

      - Dual ring Topology

      - Fiber optic media

      - Used for a redundant backbone

- NICs – Network Interface Cards

  - MAC addresses – AKA Physical Address, BIA (burned in address)

    - 48 bits

    - 12 Hexadecimal

    - Unique (No 2 MAC addresses are the same)

    - Composed of 2 Parts

      - 1st 24 bits – OUI (Organizational Unique Identifier) – who made the NIC

      - 2nd 24 bits – Serial number – Gets bigger by 1 for each NIC made

    - Used to deliver LAN transmissions

    - Cannot be changed – Burned into the NIC

- PDU – Frame

  - Source and Destination MAC address

  - FCS – Frame Check Sequence – Used for Error Detection/Correction

  - Data Itself

Layer 3 – Network Layer

- IP Addressing

  - Identifies this device on the Internet

  - Logical Address – Can be logically assigned/changed

  - DHCP – Automatically assigns IP addresses (Dynamic Host Configuration Process)

  - Two parts to an IP address

    - Network Portion – This part will not change (locked in)

    - Host portion – This part will change for each host on the network.

  - Subnet Mask – Tells which parts of the IP address are network and host

- 1 – means a network bit

- 0 – means a host bit

- Expressing a subnet mask

      - Dotted Decimal – 255.255.255.0

      - Slash Notation - /24 – Number tells how many network bits (out of 32)

      - Altering the subnet mask changes the size of your network/subnet.

  - Classes of Networks

    - Class A

      - 255.0.0.0 – Default Subnet Mask

      - Only first octet is locked

      - 16.7 million hosts on each Class A

      - First Octet value is 1-126

    - Class B

      - 255.255.0.0 – Default Subnet Mask

      - First 2 octets are locked

      - 65536 IP addresses per Class B

      - First octet is 128-191

    - Class C

      - 255.255.255.0 – Default Class C Subnet Mask

      - First 3 octets locked

      - 256 IP addresses on each Class C

      - First octet value 192-223

  - Three Types of IP Addresses

    - Network Address

      - First IP address of a subnet/network.

      - Cannot be used for a host or router interface.

      - Used to represent the entire network/subnet

      - Use with RIP in a NETWORK statement.

      - All zeros in the host portion (binary)

    - Host Address

      - Assignable to interfaces and hosts

      - Cannot be reused - each device needs its own, unique IP address

      - All of the IP addresses between the network and broadcast addresses.

    - Broadcast Address

      - Last IP address of a subnet/network.

      - Cannot be used for a host or router interface.

      - Used to send a message to everyone on that network/subnet.

      - All 1s (ones) in the host portion.  (binary)

  - Private IP Addresses

    - Can be reused

    - Will not be routed (sent to remote networks)

    - There is a private IP range for each class of network

      - Class A – 10.0.0.0 to 10.255.255.255

      - Class B – 172.16.0.0 to 172.31.255.255

      - Class C – 192.168.0.0 to 192.168.255.255

- Routing Protocols

  - Make decisions about how to get to destination networks.

  - RIP is a routing protocol.

  - Terminology

    - Metric – Measurement used to calculate the best route.  (ex:  hop count)

    - Administrative Distance – Trustworthiness of the route

      - Lowest AD wins

      - 0 – Directly Connected

      - 1 – Static Route

      - 90 – EIGRP

      - 110 – OSPF

      - 120 – RIP

Layer 4 – Transport Layer

- Handles reliability when data is sent across the Internet.

  - Three Way Handshake

    - Before any data is transmitted, sender and receiver verify communications.

      - 1st Part – Sender “Are you there?”

      - 2nd Part – Receiver “Yes.  Are you there?”

      - 3rd Part – Sender “Yes”

      - Both sides have responded to requests from the other side.

  - Acknowledgments – Receiver verifies receipt of each “chunk” of data

  - Windowing – Data transfer rate is negotiated between sender and receiver.

  - Sequencing – All “chunks” are numbered so they can be reorder as they arrive out of order.

  - Port Numbers – Different Communications use different “Channels”

    - Numbers 0 through 1023 are registered for certain protocols/applications

      - Port 80 – HTTP (web page traffic)

      - Port 20, 21 – FTP (download/upload)

      - Port 23 – Telnet (remote control using an IP address)

      - Port 25 SMTP (Simple Mail Transfer Protocol – sending email)

      - Port 53 – DNS (Domain Name Service – converting cisco.com to IP)

    - Port numbers greater than 1023 are unregistered

      - Used to keep instances of same traffic type separate

      - Multiple Browser windows

        - Source Port number is > 1023 and often randomly assigned

        - Destination port is 80

- PDU – Segment (what we call data at the transport layer)

Layer 5 Session Layer

- We build a virtual circuit between sender and receiver.

- Connection is managed two ways:

  - Web Page – Connection established – Data transferred – Connection terminated

  - Telnet – Connection established and maintained until you choose to terminate it.

- Session layer defines the set up, management and termination of these connections.

Layer 6 Presentation Layer

- Sender and receiver try to find a “common data format”.

- Universal file types are helpful

  - Images – BMP, JPG, GIF, PNG

  - Video – MPEG, Quicktime, AVI

  - Audio – MP3, Wav

- Presentation layer will attempt to convert to a known format on both sides

Layer 7 Application Layer

- We are using a program that utilizes the Internet

- Examples

  - Telnet

  - Web browser

  - World of Warcraft

  - Email

  - Instant Messaging

  - VOIP

  - Downloading/Uploading

OSI Model Recap

Layer 1 – Physical – Media – PDU Bit

Layer 2 – Data Link – LAN communications – PDU Frame

Layer 3 – Network – IP Addressing and Routing – PDU packet

Layer 4 – Transport – Reliability with Internet communications – PDU segment

Layer 5 – Session – Virtual Circuit Management

Layer 6 – Presentation – Common Data Format

Layer 7 – Application – A program requires the Internet  - PDU – Raw Data

Mnemonic Devices

Please Do Not Throw Sausage Pizza Away – Layers 1 to 7

All People Seem To Need Data Processing – Layers 7 to 1

Big First Person Shooter, Dude! – PDUs for Layer 1-4, 7