Router Commands – Esim

Below is the command to configure Lab_A.  You will have to adapt the commands for routers B through E

enable					enter enable mode, accesses more commands

configure terminal			lets you change the configuration

router rip				must turn on dynamic routing protocol (RIP)

network 192.5.5.0			must specify directly connected networks for RIP

network 205.7.5.0			ditto

network 201.100.11.0			ditto

exit					good to break up your command entry into sections

hostname lab_a				routers need names too

line vty 0 4				allow telnet sessions so others can see/modify config

password cisco				sets telnet password

login 					specifies telnet login

line console 0				allow console sessions

password cisco				sets console password

login					specifies console login

exit					good to break up your command entry into sections

enable secret class			set the overall login password

interface ethernet 0			routers have interfaces; they must be configured (LAN)

ip address 192.5.5.1  255.255.255.0	interfaces need layer 3 addresses

no shutdown				interfaces are shutdown until you undo the shutdown

interface ethernet 1			routers have interfaces; they must be configured (LAN)

ip address 205.7.5.1  255.255.255.0	interfaces need layer 3 addresses

no shutdown				interfaces are shutdown until you undo the shutdown

interface serial 0			routers have interfaces; they must be configured (WAN)

ip address 201.100.11.1  255.255.255.0	interfaces need layer 3 addresses

clock rate 56000			many serial interfaces must be clocked

no shutdown				interfaces are shutdown until you undo the shutdown

exit					good to break up your command entry into sections

ip host lab_a  192.5.5.1  205.7.5.1  201.100.11.1					DNS

ip host lab_b  219.17.100.1  199.6.13.1  201.100.11.2				DNS

ip host lab_c  223.8.151.1  204.204.7.1  199.6.13.2				DNS

ip host lab_d  210.93.105.1  204.204.7.2						DNS

ip host lab_e  210.93.105.2							DNS

exit

show run				check your work

copy run start				save your work