Texas Cluster

Part I - IP Addressing Scheme – 5 LANs, 1 Shared WAN Link

Dallas - 9900 customers		Houston - 2200 customers			El Paso - 1400 customers

Austin - 500 customers		Lubbock - 90 customers

| Subnet Size | Network Address | Subnet Mask | Wildcard Mask |
| --- | --- | --- | --- |
|  | 185.X.128.0 |  |  |
| Shared WAN (5 connections) |  |  |  |

Part II.  Configuration Details

- IP Addressing Rules - LANS

  - The Router’s FastEthernet 0/1 interface gets the first usable for the LAN it connects to

  - PCs get the 2nd usable

  - Laptops get 3rd usable

  - Server gets last usable

  - Printers get second to last usable

  - DNS should be set to 8.8.8.8 for all devices.

  - Switches don’t need to be assigned IP Addresses this time.

- IP Addressing Rules – Shared WAN link

  - There are no serial interfaces to be configured in Texas, just a shared WAN link that uses a switch to connect five different LANs.

  - FastEthernet 0/0 on each router connects to Texas-Switch.  These interfaces will all need to be assigned an IP address from this shared WAN link.  It will use a /29 subnet mask since there are 5 IP addresses needed to connect the five routers.

- Router Configuration should include the following:

  - Hostname

  - Save the configuration

  - Serial interfaces can be configured with clock rate matching that shown within the topology.

  - Be sure to all set your Bandwidth statements on all serial interfaces so OSPF will properly calculate the correct cost to get to different parts of the topology.

- Routing Protocol

  - OSPF

    - Default Route should be built and propagated from Dallas toward Denver

    - Each router will be configured with OSPF and require 2 network statements:

      - 1 Network statement for its connected LAN

      - 1 Network statement for the shared WAN Link

  - Static Routing

    - Don’t forget to build the default router manually on Dallas (toward Denver)

    - Lubbock will have OSPF configured, but will also add in its own static routes to the other LANs.

    - Make sure you use the next-hop static route method, since exit-interface doesn’t provide enough information.		IP ROUTE <Network> <Subnet Mask> <Next-hop IP>