VLAN Commands

SWITCH COMMANDS

- VLAN DATABASE				6 Switches

- VLAN (#) NAME (NAME)			1 server

- VTP MODE CLIENT				1 transparent

- VTP MODE SERVER			4 client

- VTP MODE TRANSPARENT 		5 vlan database entries

- VTP DOMAIN (NAME)			add 1, delete 1, change 1

- VTP PASSWORD (PASSWORD)

- SWITCHPORT MODE TRUNK

- SWITCHPORT TRUNK NATIVE VLAN (VLAN #)

- SWITCHPORT MODE ACCESS

- SWITCHPORT ACCESS VLAN (#)

- SHOW VLAN

- SHOW VTP STATUS

- SWITCHPORT PORT-SECURITY MAC-ADDRESS 1234.5678.9abc

- SWITCHPORT PORT-SECURITY MAC-ADDRESS STICKY

- SWITCHPORT PORT-SECURITY MAXIMUM (#)

- SWITCHPORT PORT-SECURITY VIOLATION SHUTDOWN

- SWITCHPORT TRUNK NATIVE VLAN (#)

ROUTER COMMANDS

- INTERFACE F0/0.1 (SUBINTERFACE)

- ENCAPSULATION DOT1Q (VLAN#)

- ENCAPSULATION DOT1Q (VLAN#) NATIVE

VLAN AND VTP REMINDERS

- Each side of a switch/switch or switch/router connection must be set to trunk if it is to carry VLAN information.

- In order to establish inter-VLAN communications, each vlan must be given its own subnet and IP address range.  Further, a separate subinterface must be created on the FastEthernet interface that functions as the default gateway.  Dot1Q encapsulation will be set on the router side and used to associate a subinterface with a specific subnet.

- VTP is used to carry VLAN information from a switch acting as a VLAN server to other switches functioning as VLAN clients.  It order for this to work, we have to establish a dedicated VLAN called the NATIVE VLAN that will distribute the VLAN information from the server to the clients.  Here’s the steps you will follow:

  - Create all needed VLANs and a native VLAN on the main switch (server).  Create a domain name and a password.

  - Put all other switches in client mode.  They should be set with the domain.  Add the password.

  - All switch to switch connections should be set to trunk and to use the native vlan.

VLAN DATABASE

- VLAN Database will be used to create VLANs.  Each VLAN should have a name and a number.

ACCESS MODE

- Any switchport that connects to a host should be set in access mode and associated with a specific VLAN.

- You must configure this from the individual switchport  (ex:  INT F2/1)